## Slide 1
THz channel factors estimation using sub-6GHz channel information
Objective : 1. Train a DL model to read 2.4GHz channel matrix and predict 100GHz channel factors – Angles of Departure and Arrival, Time of Arrival, Pathloss, and Phase Difference on Arrival.
2. Use estimated THz channel factors for optimal beamformer prediction.
Scenario :
100,000 users (elevation 2m above surface) located in Chicago downtown area, in a rectangular block of dimensions roughly 500m * 40m with sub-6GHz/THz tower on one boundary of the block.
Scenario Parameters
Centre Frequency | 2.4GHz | 100GHz
Antenna array length | 4 | 64
Bandwidth | 20MHz | 500MHz
No. of OFDM subcarriers | 64 | 64
BS Antenna height | 8m | 8m
User Antenna height | 2m | 2m
Propagation Model (MATLAB) | sbr + gas + cloud | sbr + gas + cloud
Max no. of paths | 8 | 4

## Slide 2
Input
(Sub-6GHz Channel Matrix 2D Image)
4 ‘Convolution-Based’ Layers
Dense
Layer
Output
(THz parameters)
…
3 Dense Layers
Output
(Optimal Beamformer)
Conv
Maxpool
IN
ReLU
Dropout
Conv
Maxpool
IN
ReLU
Dropout
GAP
Dense
ReLU
Dropout
Dense
Softmax
CNN based THz channel factors estimation
ANN based beamformer prediction

## Slide 3
Neural Network Hyperparameters
Hyperparameter | THz estimation | Beamformer Prediction
Conv Kernel Size | (2,4) | -
Conv no. of filters | 32 | -
Maxpool Kernel Size | (2,2) | -
Maxpool stride | 2 | -
Dense layer dimension | - | 64
No. of training samples | 80,000 | 80,000
No. of test samples | 20,000 | 20,000
No. of epochs | 100 | 100
Task Type | Regression | Classification
Optimizer | SGD | Adam
Initial Learning Rate (LR) | 1.00 * 10-3 | 1.00 * 10-2
LR Decay Factor | 0.1 | -
LR Decay Schedule | 80 epochs | -
Momentum | 0.85 | -
Dropout | 0.2 | 0.2

## Slide 4
Performance Evaluation

## Slide 5
Ongoing Work
Use CNN predicted THz channel factors to obtain the BS (out of 3 given BSs) providing best THz channel conditions / highest spectral efficiency for a particular user.
Input : Sub-6GHz channel matrices from user to 3 BSs
Algorithm : (a) Individual sub-6GHz channel matrix -> THz channel factors
(b) THz channel factors from 3 BSs -> best BS via DL based classification
Output : best BS index for that user
Future channel condition aware scheduling
(a) Can the deepMIMO dataset be used in some way for a user grouping/ scheduling task?
(b) Is there a way to include interference data to obtain optimal beamformer from deepMIMO dataset?

## Slide 6
Sub-6GHz channel matrix (2D Image Format Input)
Convolutional Neural Network Followed By Global Average Pooling Layer
THz Channel Parameters
Dense Neural Network Followed by Softmax Layer
Beam Selection
Combined System Model