## Slide 1
THz channel estimation using sub-6GHz channel information
Objective : Train an ML model to read 2.4GHz channel matrix and predict 100GHz channel parameters – Angles of Departure and Arrival, Time of Arrival, Pathloss, and Phase.
Scenario :
100,000 users (elevation 2m above surface) located in Chicago downtown area, in a rectangular block of dimensions roughly 500m * 40m with sub-6GHz/THz tower on one boundary of the block.
Parameters
 | 2.4GHz | 100GHz
Antenna array dimension | 1*4*1 | 1*64*1
Bandwidth | 20MHz | 500MHz
No. of OFDM subcarriers | 64 | 64

## Slide 2
ML model Parameters
Input : Sub-6GHz channel matrix of dimension (4(antenna array length) * 64(no. of subcarriers)), for each user, flattened (real and imaginary parts separated as well), to form vector of length 512.
Output : THz channel parameters (AoD, AoA, Phase, Pathloss, ToA), for each user
Model Parameters :
Layer | No. of Units | Activation
Dense | 128 | ReLU
Dense | 128 | ReLU
Dense | 128 | ReLU
Dense | 128 | ReLU
Dense | 7 | -
Regression | 7 | -
Architecture
Weights Initializer | Random
Solver | Adam
Training Epochs | 100
No. of Inputs | 100,000
Batch Size | 200
Shuffle | Every epoch
Initial Learning Rate(LR) | 0.001
LR Drop Factor | 0.5
LR Drop Period | 20 epochs
L2 Regularization | 0.0001
Loss | Mean Squared Error
Neural Network Parameters

## Slide 3
…
…
…
…
…
…
…
Input Vector of Length 512 (Sub-6GHz channel matrix)
4 hidden layers on 128 units each
Hidden layer with 7 units
Output THz channel params (AoD, AoA, Pathloss, ToA, Phase)
ReLU
Applied Neural Network Diagrammatic Representation
Issue : Phase Prediction significantly inaccurate

## Slide 4
Changes Introduced
Sub-6GHz channel matrix given as 2D image format [magnitude,phase] (256,2)
CNN layer introduced to extract spatial features
Dense Neural Network based Beamformer Selection from predicted channel parameters
Regression error reduced because of CNN being able to utilize 2D array instead of flattened array input to Dense Neural Network
Phase error mitigated.

## Slide 5
Sub-6GHz channel matrix (2D Image Format Input)
Convolutional Neural Network Followed By Global Average Pooling Layer
THz Channel Parameters
Dense Neural Network Followed by Softmax Layer
Beam Selection
Combined System Model